## Slide 1: Site Drainage Areas (SDAs) vs. Contributing Drainage Areas (CDAs)
TAG THIS PRESENTATION @DOEE_DC
Notes: Site Drainage Area (SDA) – The area that drains stormwater from the site to a single discharge point or sheet flows from a single area off the site.
Contributing drainage area (CDA) – Area contributing runoff to a BMP.

## Slide 2
Building is undergoing a complete renovation.
Surrounding land is being regraded with new sidewalks and construction of an underground parking facility.
Building = Major Substantial Improvement (0.8”)
Land Area = Major Land Disturbing (1.2”)

## Slide 3
Site Drainage Areas
SDA#2 = 66,971 ft2
SDA#1 = 65,496 ft2

## Slide 4: Site Drainage Area #1
@DOEE_DC
Major Land Disturbing (1.2-inch) | Land Area (ft2) | Rv | SWRv (ft3)
Impervious Cover (sidewalks, etc.) | 11,197 | 0.95 | 1,064
Compacted Cover (grass, landscaping) | 43,685 | 0.25 | 1,092
BMP (bioretention) | 1,489 | 0.95 | 141
MLD Total |  |  | 2,297
Major Substantial Improvement (0.8-inch) | Land Area (ft2) | Rv | SWRv (ft3)
Impervious Cover (building) | 9,125 | 0.95 | 578
MSI Total |  |  | 578
SDA#1 = 65,496 ft2
Total | 65,496 |  | 2,875

## Slide 5: Site Drainage Area #2
@DOEE_DC
SDA#2 = 66,971 ft2
Major Land Disturbing (1.2-inch) | Land Area (ft2) | Rv | SWRv (ft3)
Impervious Cover (sidewalks, etc.) | 11,704 | 0.95 | 1,112
Compacted Cover (grass, landscaping) | 27,289 | 0.25 | 682
BMP (bioretention, green roof) | 9,878 | 0.95 | 938
MLD Total |  |  | 2,732
Major Substantial Improvement (0.8-inch) | Land Area (ft2) | Rv | SWRv (ft3)
Impervious Cover (building) | 18,100 | 0.95 | 1,146
MSI Total |  |  | 1,146
Total | 66,971 |  | 3,878

## Slide 6
Total SWRv for Site
@DC
@DOEE_DC
Site Drainage Area #1 | 2,875 ft3
Site Drainage Area #2 | 3,878 ft3
Total = 6,753
Notes: Similar model to DC Snow Teams

## Slide 7
BMP Locations
@DC
@DOEE_DC
Bioretention
Green Roof
Notes: Similar model to DC Snow Teams

## Slide 8
@DC
@DOEE_DC
A
B
C
D
E
Site Drainage Areas
Contributing Drainage Areas
Notes: SDAs based on proposed land cover. Must consider BMPs. If sheet flow is going to generally the same place as a sewer lateral as in the red/yellow area here, it can be considered the same SDA. The intent is to treat the site not just a tiny area.

## Slide 9
@DC
@DOEE_DC
SDA#1 = 65,496 SF
SDA #1 SWRv (1.2-inch) = | 2,875 ft3
Retention Volume Bioretention | 2,576 ft3
Actual Retention Value | 2,576 ft3
Land Cover Type | CDA Area (ft2) | Rv | Max. Retention Vol. (ft3) (1.7-in)
Impervious Cover | 18,067 | 0.95 | 2,432
Compacted Cover | 36,566 | 0.25 | 1,295
BMP | 1,489 | 0.95 | 200
Total | 56,122 |  | 3,927
A
Notes: Similar model to DC Snow Teams

## Slide 10
Example #2
@DC
@DOEE_DC
SDA#2 = 66,981 SF
SDA #2 SWRv (1.2-inch) = | 3,878 ft3
BMP | Max. Retention Vol. (ft3) (1.7-inch) | BMP Retention Volume (ft3)
B | 997 | 1,047
C | 1,314 | 1,402
D | 923 | 859
E | 1,241 | 1,157
Total | 4,475 | 4,465
Retention Value | 4,327 ft3
B
C
D
E
Notes: How do we deal with the bioretention area? Impervious because SWRv is a calculation of how much water will get to the bmp. (nearly) All the water that lands on a bmp gets to it.

## Slide 11
Total SWRv for Site
@DC
@DOEE_DC
Site Drainage Area #1 | 2,875 ft3
Site Drainage Area #2 | 3,878 ft3
Total = 6,753
Actual Retention Volume BMP A | 2,576 ft3
Actual Retention Volume BMPs B - E | 4,327 ft3
Met their stormwater obligation!
Total = 6,903
Notes: Met 50% min for SDA 1
Overcontrol on SDA results in greater than 100% total for the site. (assuming VAA met)