## Slide 1: Stormwater BMP Specifications
Chapter 3
TAG THIS PRESENTATION @DOEE_DC
Notes: Chapter 3 of the stormwater management guidebook covers the stormwater bmp specifications

## Slide 2: Best Management Practices (BMPs)
@DOEE_DC
3.2 Green Roofs | 3.9 Open Channel Systems
3.3 Rainwater Harvesting | 3.10 Ponds
3.4 Impervious Surface Disconnection | 3.11 Stormwater Wetlands
3.5 Permeable Pavement Systems | 3.12 Storage Practices
3.6 Bioretention | 3.13 Proprietary Practices
3.7 Filtering Systems | 3.14 Tree Planting and Preservation
3.8 Infiltration | 
Notes: In this video we’ll discuss green roofs

## Slide 3
Specification Format
@DC
@DOEE_DC
Feasibility Criteria
Conveyance Criteria
Pretreatment Criteria
Design Criteria
Landscaping Criteria
Construction Sequence
Maintenance Criteria
Retention Value Calculations
References
Notes: the guidebook is arranged such that the specifications for each bmp type are laid out in the same format and includes the following subsections

## Slide 4
3.2 Green Roofs
Notes: US Tax Court

## Slide 5
Green Roof Specification
@DC
@DOEE_DC
Preferred practice in high intensity redevelopment areas
Allow for many different vendors and systems
Follow ASTM specifications

## Slide 6
Green Roofs
@DC
@DOEE_DC
Major element of compliance at urban development sites
Extensive or Intensive
Structural design considerations
High installation cost
Increased roof longevity
Additional urban environmental benefits

## Slide 7
@DC
@DOEE_DC
Intensive
Extensive

## Slide 8
Green Roof Feasibility Criteria
@DC
@DOEE_DC
Structural capacity of roof
Roof pitch
Setbacks from HVAC, building edge
Compliance with building codes, fire code
Maximum contributing drainage area to the green roof is no more than 100% of the green roof area
Flow dissipation required to spread flow and prevent erosion
Notes: HVAC over green roof does not get credit unless it meets certain criteria
Very important to show reviewer how the CDA gets to the green roof.

## Slide 9
Conveyance and Pretreatment
@DC
@DOEE_DC
Drainage layer and roof drains must safely convey overflows
No requirements for pretreatment

## Slide 10
Green Roof Design Criteria
@DC
@DOEE_DC
Material specifications for each layer
The drainage layer can be combined with the growing media layer

## Slide 11
Green Roof Design Criteria
@DC
@DOEE_DC
Solar panels, HVAC equipment, or other structures can be installed above a green roof as long as these minimum dimensions are met
Notes: Purpose of this is twofold:
1. space to walk in between for maintenance
2. Sun and rain contact with green roof
Flexible for different size solar panels but space between must be adjusted.
HVAC not sloped so it must be 2.5 above

## Slide 12
Green Roof Design Criteria
@DC
@DOEE_DC
Sizing Equation
Sv = storage volume (ft3)
SA = green roof area (ft2)
d = media depth (in) (minimum 3 in.)
η1 = verified media maximum water retention (use 0.10 as a baseline default in the absence of verification data)
DL = drainage layer depth (in.) (if the drainage layer is combined with the media layer, then this value is 0)
η2 = verified drainage layer maximum water retention (use 0.00 as a baseline default in the absence of verification data)
Notes: ASTM standard test for max water retention.

## Slide 13
Green Roof Landscaping Criteria
@DC
@DOEE_DC
Plants need to resist and withstand:
Drought
Fire
Wind
Snow-loading
Heat-stress

## Slide 14
Green Roof Landscaping Criteria
@DC
@DOEE_DC
Temporary irrigation is recommended for establishment or drought
Permanent irrigation is prohibited for extensive green roofs
Intensive green roofs with irrigation have a reduced retention value
Notes: Stormwater needs a roof not filled with irrigation water
Key is permanent irrigation

## Slide 15
Green Roof Retention Value Calculations
@DC
@DOEE_DC
Unirrigated Retention Value = Sv = 100% of Storage Volume in Media and Drainage Layer
Irrigated Retention Value = 50% of Storage Volume in Media and Drainage Layer
Notes: Admittedly not scientific enough 50% retention value for intensive GR w/ permanent irrigation