## Slide 1: Stormwater BMP Specifications
Chapter 3
TAG THIS PRESENTATION @DOEE_DC
Notes: Chapter 3 of the stormwater management guidebook covers the stormwater bmp specifications

## Slide 2: Best Management Practices (BMPs)
@DOEE_DC
3.2 Green Roofs | 3.9 Open Channel Systems
3.3 Rainwater Harvesting | 3.10 Ponds
3.4 Impervious Surface Disconnection | 3.11 Stormwater Wetlands
3.5 Permeable Pavement Systems | 3.12 Storage Practices
3.6 Bioretention | 3.13 Proprietary Practices
3.7 Filtering Systems | 3.14 Tree Planting and Preservation
3.8 Infiltration | 

## Slide 3
Specification Format
@DC
@DOEE_DC
Feasibility Criteria
Conveyance Criteria
Pretreatment Criteria
Design Criteria
Landscaping Criteria
Construction Sequence
Maintenance Criteria
Retention Value Calculations
References
Notes: the guidebook is arranged such that the specifications for each bmp type are laid out in the same format and includes the following subsections

## Slide 4
3.6 Bioretention

## Slide 5
Bioretention Specification
@DC
@DOEE_DC
Popular practice on sites with some surface land available
Multiple design options and sizes

## Slide 6
B-1 Traditional Bioretention
@DC
@DOEE_DC

## Slide 7
B-2 Streetscape Bioretention
@DC
@DOEE_DC
Notes: Not common in DC because of parking

## Slide 8
B-3 Engineered Tree Pits
@DC
@DOEE_DC
Notes: More common due to wide sidewalks

## Slide 9
B-4 Foundation Planters
@DC
@DOEE_DC

## Slide 10
B-5 Residential Rain Gardens
@DC
@DOEE_DC

## Slide 11
Bioretention Feasibility Criteria
@DC
@DOEE_DC
Works for all soil types and most site conditions
4 to 5 feet of head
No irrigation or baseflow
Liner required for hotspots

## Slide 12
Conveyance Criteria and Pretreatment
@DC
@DOEE_DC
Conveyance: Off-line vs. On-line
  On-line requires overflow device
Pretreatment Required
  Pretreatment Cell
  Grass Filter Strips
  Stone Diaphragm
Notes: Off-line shown here, can’t overflow because of bypass in large storms
In-line requires overflow to handle 15 yr storm w/ 3” freeboard.
Pretreatment helps with maintenance of a single point

## Slide 13
Standard Bioretention Design
@DC
@DOEE_DC
  Underdrain designs without enhanced features
  At least 18” media
  60% retention value for the design storm captured
  Additional TSS removal
  Oversizing practice can result in meeting full criteria

## Slide 14
Enhanced Bioretention 1
(with Underdrain)
@DC
@DOEE_DC
Underdrain designs with minimum 9” deep infiltration sump and at least 24” filter media
Sump storage volume must infiltrate within 72 hours (Ksat = 0.1 ft/day)
100% retention value for the design storm captured

## Slide 15
Enhanced Bioretention 2
(full Infiltration)
@DC
@DOEE_DC
At least 18” filter media
Full storage volume must infiltrate within 72 hours
100% retention value for the design storm captured

## Slide 16
Bioretention Design Criteria
@DC
@DOEE_DC
Ponding depth:
  Maximum 18”, Minimum 3”
3:1 side slopes or vertical drop
Must have an observation well

## Slide 17
Bioretention Design Criteria
@DC
@DOEE_DC
Maximum filter media depth
  The runoff coefficient of the CDA to the BMP (RvCDA)
  The bioretention ratio of BMP surface area to the BMP CDA (SA:CDA) (in percent)
  See Table 3.20
Notes: Imagine a very deep small practice. Storm will be over before the water percolates down to the bottom.
Table based on modeling. Key factors on axes.

## Slide 18
Table 3.20 Determining Maximum Filter Media Depth (feet)
@DC
@DOEE_DC
Notes: During high intensity storm events, it is possible for the bioretention to fill up faster than the collected stormwater is able to filter through the soil media. This is dependent upon the surface area of the BMP (SA) relative to the contributing drainage area (CDA) and the runoff coefficient (Rv) from the CDA. To ensure that the design runoff volume is captured and filtered appropriately, a maximum filter media depth must not be exceeded (see Table 3.24). The maximum filter media depth is based on the runoff coefficient of the CDA to the BMP (RvCDA) and the bioretention ratio of BMP surface area to the BMP CDA (SA:CDA) (in percent). The applicable filter media depth from Table 3.21 should be used as dmedia in Equation 3.5.
Hardest part is the medium size practices. There may not be enough rain at the beginning and end of a storm to fill up the media.
Recommend maximizing ponding depth before maxing media depth.

## Slide 19
Bioretention Design Criteria
@DC
@DOEE_DC
Filter Media Specifications (based on weight)
  80%-90% sand
  10%-20% silt and clay
  Maximum 10% clay
3%-5% organic amendments
P concentrations between 5 and 15 mg/kg (Mehlich I) or 18 and 40 mg/kg (Mehlich III)
Notes: Because this is by weight and silt/clay much lighter than sand the media feels like a sandy topsoil from the organic ammendments.
Key to note on organic amendments is max P concentrations to prevent exporting P from the media itself.

## Slide 20
Table 3.19 Summary of Filter Media Criteria for Bioretention
@DC
@DOEE_DC

## Slide 21
Bioretention Design Criteria
@DC
@DOEE_DC
Sizing Equation
Where:
Sv = total storage volume of bioretention (ft3)
SAbottom = bottom surface area of bioretention (ft2)
dmedia = depth of the filter media, including mulch layer (ft)
ηmedia = effective porosity of the filter media (typically 0.25)
dgravel = depth of the underdrain and underground storage gravel layer, including choker stone (ft)
ηgravel = effective porosity of the gravel layer (typically 0.4)
SAaverage = the average surface area of the bioretention (ft2)
dponding = the maximum ponding depth of the bioretention (ft)
Notes: Long equation to say the volume of the water that fits in the pond, the gravel, and the media.
Diagram of top and bottom surface area to clarify. Top area is the bmp area.

## Slide 22
Bioretention Tree Pit Design Criteria
@DC
@DOEE_DC
Notes: SBSS specs nearly the same as bioretention media. So it can be counted toward retention if it meets P requirements and overall average ponding depth is 3 in.

## Slide 23
Bioretention Tree Pit Design Criteria
@DC
@DOEE_DC
The filter media must be connected to media under the sidewalk
The average depth of ponding must be at least 3 inches
Sand based structural soil (SBSS) can be used as filter media with the following criteria:
  The SBSS must meet the same phosphorus content limits
  If the SBSS is to be compacted beyond the DDOT Green Infrastructure Standards maximum compaction for bioretention, it shall be assigned a porosity of 0.10

## Slide 24
Bioretention Design Criteria
@DC
@DOEE_DC
Surface Cover Options
  Mulch and perennial vegetation
  Turf
  Stone with perennial vegetation
Notes: Stone can be used instead of mulch (not a good idea at schools). Plants are important.

## Slide 25
Bioretention Landscaping Criteria
@DC
@DOEE_DC
Landscaping is critical to bioretention function
Planting plan must be submitted
Consider:
  Maintenance
  Plant suitability
  Native plants
Notes: Many options of cover available – plant lists included in spec.
Maintenance should inform landscape plan.