## Slide 1: Stormwater BMP Specifications
Chapter 3
TAG THIS PRESENTATION @DOEE_DC
Notes: Chapter 3 of the stormwater management guidebook covers the stormwater bmp specifications

## Slide 2: Best Management Practices (BMPs)
@DOEE_DC
3.2 Green Roofs | 3.9 Open Channel Systems
3.3 Rainwater Harvesting | 3.10 Ponds
3.4 Impervious Surface Disconnection | 3.11 Stormwater Wetlands
3.5 Permeable Pavement Systems | 3.12 Storage Practices
3.6 Bioretention | 3.13 Proprietary Practices
3.7 Filtering Systems | 3.14 Tree Planting and Preservation
3.8 Infiltration | 

## Slide 3
Specification Format
@DC
@DOEE_DC
Feasibility Criteria
Conveyance Criteria
Pretreatment Criteria
Design Criteria
Landscaping Criteria
Construction Sequence
Maintenance Criteria
Retention Value Calculations
References
Notes: the guidebook is arranged such that the specifications for each bmp type are laid out in the same format and includes the following subsections

## Slide 4
3.7 Filtering Systems
@DC
@DOEE_DC
0% Retention Value
Accepted TSS removal practice
Usually installed to meet treatment requirements in vehicular access areas
Notes: Less often now because of retention approach.

## Slide 5
3.8 Infiltration
@DC
@DOEE_DC
100% Retention Value for water that infiltrates in 72 hours
Requires field-verified saturated hydraulic conductivity
Notes: Simplified bioretention with just infiltration, no evapotranspiration

## Slide 6
3.9 Open Channels
@DC
@DOEE_DC
Dry swale, wet swale, and grass channel
Not high priority BMPs
Dry Swale = 60% Retention + accepted TSS removal practice
Wet Swale = 10% Retention + accepted TSS removal practice
Grass Channel = 10% - 30% Retention
Notes: Dry swale treated just like bioretention

## Slide 7
3.10 Stormwater Ponds &
3.11 Stormwater Wetlands
@DC
@DOEE_DC
Rarely used
10% retention value
Accepted TSS removal practice
Notes: 10% retention of permanent pool storage

## Slide 8
3.12 Storage Practices
@DC
@DOEE_DC
No retention or TSS removal value
Intended only for detaining large storm events
Detention routing calculations required

## Slide 9
3.13 Proprietary Practices
@DC
@DOEE_DC
Approval procedures involve field studies and/or lab tests
Variable retention and TSS removals
Generally low retention value and high TSS removal
Approval follows NJDEP Protocol
Appendix T

## Slide 10
3.14 Tree Planting and Preservation
@DC
@DOEE_DC
Gives Retention Value for individual trees
Landscape professional tree inventory for preservation
Planting plan for new tree planting
Proper planting and maintenance required
Trees must be within the LOD
Notes: 1500 cf for a single tree, 1000 if shared

## Slide 11
3.14 Tree Planting and Preservation
@DC
@DOEE_DC
Minimum rootable soil volume requirements
  Small trees
    600 cf single planting
    400 cf (each) shared space
  Large trees
    1500 cf single planting
    1000 cf (each) shared space
Soil considered “rootable” to 3’ deep and 16’ (small) or 27’ (large) radius
+
16’ – 27’
Building
Standard Pavement
Adjacent Property
Rootable soil to max 3’ depth
+
New tree
Notes: 1500 cf for a single tree, 1000 if shared

## Slide 12
Tree Planting Preservation Retention Values
@DC
@DOEE_DC
Preserved Trees
  Small trees (< 40 ft avg. mature spread) = 10 ft3
  Large trees (> 40 ft avg. mature spread) = 20 ft3
  Special trees (> 44 in. circumference) = 30 ft3
  Heritage trees (> 100 in. circumference) = 40 ft3
Planted Trees
  Small trees (< 40 ft avg. mature spread) = 5 ft3
  Large trees (> 40 ft avg. mature spread) = 10 ft3
Notes: Preserving an existing tree retains more water than a newly planted tree
Trees planted in bmps get credit for both the bmp and the tree
Green Area Ratio has resources on tree spread etc.