## Slide 1: Reconstruction of Existing Public Right-of-Way
MEP tailored to the streetscape portion of a Major Regulated Project
TAG THIS PRESENTATION @DOEE_DC
Notes: In this video we’ll cover reconstruction of existing public right of way. We’ll learn when stormwater regulations apply for work in the prow and how to meet stormwater requirements to the maximum extent practicable.

## Slide 2
@DOEE_DC
Notes: For WQTv, P = 3.2 inches

## Slide 3
@DOEE_DC

## Slide 4: When PROW MEP applies…
@DOEE_DC
Reconstruction of Existing Public right-of-way
Type 1: Federal or municipal
  roads, alleys, sidewalks, trails, etc.
Type 2: Private development
  adjacent sidewalks and alleys

## Slide 5: When PROW MEP does not apply…
@DOEE_DC
A major regulated project that does not disturb the adjacent public right-of-way
Voluntary retrofits of existing PROW
PROW disturbance that is limited to
  Trenches
  Driveways
  Utilities
  Aprons
  Minor disturbance
Disturbance of new PROW that was not previously PROW

## Slide 6: Principles of PROW MEP include…
@DOEE_DC
Maximize BMP placement
Maximize BMP sizing
Innovate--integrate “green” with “grey” infrastructure
Minimize impervious widths
Maximize land cover types with little stormwater runoff
Maximize tree canopy
  planting or preserving trees, amending soils, increasing soil volumes and connecting tree roots with stormwater runoff
Use impervious surface disconnection strategies
  e.g., draining sidewalk area to continuous tree planting strip
Manage comingled stormwater runoff
  prioritize the conveyance and control of roadway runoff
  Over-control the roadway runoff beyond LOD to compensate for less retention elsewhere
Use porous pavement or pavers for low traffic roadways, on-street parking, shoulders or sidewalks
Integrate BMPs into traffic calming measures
Notes: Database calculates the runoff volume using the SCS method used in TR-55

## Slide 7: Parcel PROW MEP steps include…
@DOEE_DC
Calculate SWRv
Prioritize managing roadway runoff inside the curb line
Place, size and design PROW BMPs to maximize retention
  Stormwater Management Guidebook Chapter 3 BMP specifications
  Stormwater Management Guidebook Appendix B BMP priorities and limitations
  DDOT LID Standards and Specifications
    dc.gov/DC/DDOT/Projects+and+Planning/Environment/Low+Impact+Development

## Slide 8: Design Example: Scenario
@DOEE_DC
Corner property includes 200 ft x 10 ft adjacent PROW disturbance (sidewalk)
SWRv = 1.2 in x (0.95x100%) x 2000 ft2 x 7.48/12
SWRv = 1,421 gallons
Poor infiltration rate on site
Sufficient head available for underdrain connections.

## Slide 9: Design Example: Site Plan
@DOEE_DC

## Slide 10: Design Example: Limitations
@DOEE_DC
ADA Crossing Requirements

## Slide 11: Design Example: Limitations
@DOEE_DC
Driveways

## Slide 12: Design Example: Limitations
@DOEE_DC
Bus Stop

## Slide 13: Design Example: Limitations
@DOEE_DC
Building Exist and 5’ – Wide Sidewalk

## Slide 14: Design Example: Limitations
@DOEE_DC
Utilities

## Slide 15: Design Example: Limitations
@DOEE_DC
Existing Trees

## Slide 16: Design Example: Limitations
@DOEE_DC
Bioretention

## Slide 17: Design Example: Limitations
@DOEE_DC
Permeable Pavement considered, but trees and utilities limit space available, and much of remaining sidewalk drains to bioretention area.

## Slide 18: Design Example: Results
@DOEE_DC
SWRv Achieved:
3 existing trees x 20 ft3 x 7.48 = 449 gallons
220 ft2 bioretention area (with shallow ponding) provides 823 gallons of storage
  823 gallons x 0.6 = 494 gallons
SWRv Achieved = 943 gallons
Required SWRv not met, but MEP process followed.

## Slide 19: Design Example: Results
@DOEE_DC
Recalculate SWRv for Reduced Impervious Cover:
SWRv = 1.2 in x (0.95 x 84% + 0.25 x 16%) x 2000 ft2 x 7.48/12
SWRv = 1,254 gallons
Poor infiltration rate on site
Sufficient head available for underdrain connections.